## Slide 1
GEOSPATIAL BUILDING BLOCK | HOW IT WORKS
From process contract to comparable imagery
Kernel architecture, execution lifecycle, and a runnable Sentinel-2 + DJI harmonization example
SENTINEL-2 REFERENCE
DJI COMPARISON
Revision 2 | 15 September 2026 | Architecture, contracts, execution, and evidence

## Slide 2
REUSABLE CAPABILITY WITH OBSERVABLE BEHAVIOR
What is a Geospatial Building Block?
Geospatial Building Block | Sentinel-2 + DJI
2
INPUT PROFILE
STAC, GeoTIFF, GeoJSON, or a mapped custom profile
ALGORITHM CONTRACT
Process identity, accepted semantics, parameters, runtime
TYPED OUTPUT
Declared identity, spatial/temporal scope, media type
EVIDENCE
Execution ID, input/output references, validation result
Metadata are context-dependent. The kernel dynamically creates contracts that bind the relevant data and process context, then harmonizes them through shared semantics, behavior, and evidence.
• No fixed metadata schema is sufficient for every dynamic workflow
• Discoverable through contracts: logical representations of data, processes, and their context
• Context-specific metadata remain useful inside the declared contract
• Executable and auditable through shared framework rules

## Slide 3
THE KERNEL HAS FOUR COOPERATING LAYERS
Functional contract and interface bindings
Geospatial Building Block | Sentinel-2 + DJI
3
INTERFACE BINDINGS
REST | OGC API - Processes | OpenAPI | openEO | Records
FUNCTIONAL CONTRACT
Adapt input profile -> validate -> execute -> publish typed output
PROCESS IMPLEMENTATION
CWL graph + Python/GDAL/Rasterio/TorchScript + runtime environment
SEMANTICS + EVIDENCE
Process-Type Register | STAC | quality report | checksums | W3C PROV
Interface choice can vary per Building Block; the evidence contract remains stable.

## Slide 4
EXECUTION LIFECYCLE
How a request moves through the Building Block
Geospatial Building Block | Sentinel-2 + DJI
4
1
DISCOVER
Read kernel metadata and process semantics
2
ADAPT
Map STAC/raster inputs to the algorithm contract
3
EXECUTE
Run CWL locally or submit the job to REANA
4
VALIDATE
Apply grid, quality, and policy acceptance gates
5
PUBLISH
Return typed assets, STAC metadata, and provenance
Failure is also a typed result: invalid inputs or failed thresholds stop publication and preserve diagnostic evidence.

## Slide 5
IMAGERY HARMONIZATION BUILDING BLOCK
Example: two workflows, one shared contract
Geospatial Building Block | Sentinel-2 + DJI
5
Sentinel-2 L2A RGB
Co-register + reproject
4x AI super- resolution
Reference image + histogram
DJI frames + poses + DSM
Photogrammetric orthomosaic
Area downsampling
Masked histogram matching
COMMON GRID + QUALITY GATE
COGs | STAC Items | W3C PROV | QC metrics

## Slide 6
EXECUTABLE PROCESSING
Workflow 1: Sentinel-2 establishes the reference
Geospatial Building Block | Sentinel-2 + DJI
6
01
Validate
L2A level, RGB bands, cloud and nodata masks
02
Align
Reproject and co-register to AOI and target CRS
03
Enhance
TorchScript 4x inference or labelled bicubic demo
04
Profile
256-bin masked histograms and robust quantiles
05
Publish
COG, target grid, QC, STAC, and provenance
Interpretation product, not new optical truth
• Preserve the original 10 m source link
• Validate tensor shape, scale, target resolution, and model checksum
• Apply cloud/nodata masks during inference and histogram sampling

## Slide 7
PHOTOGRAMMETRY HANDOFF + EXECUTABLE PROCESSING
Workflow 2: DJI conforms to the reference
Geospatial Building Block | Sentinel-2 + DJI
7
RAW INPUTS
• Images
• Calibration
• RTK/PPK or poses
• DEM/DSM
• Optional GCPs
PHOTOGRAMMETRY
• Camera model
• Tie points
• Dense surface
• Orthomosaic
• Checkpoint RMSE
HARMONIZATION
• Exact target grid
• Area/average kernel
• Antialiasing
• Quantile matching
• Mask preservation
COMPARABLE DJI COG
Why no AI downsampler? Area aggregation is deterministic, spectrally traceable, and easier to validate.

## Slide 8
WHAT MAKES THE OUTPUTS COMPARABLE
The handoff is a machine-readable contract
Geospatial Building Block | Sentinel-2 + DJI
8
SPATIAL CONTRACT
• Same CRS and affine transform
• Same width, height, extent, and 2.5 m grid
• Same RGB band order, dtype, range, and nodata
• Separate cloud, shadow, saturation, and validity masks
RADIOMETRIC CONTRACT
• Reference profile uses valid common overlap
• Per-band clipped quantile mapping
• Before/after histogram distances retained
• Time, sun angle, and view geometry remain explicit
Histogram similarity supports interpretation; it does not erase seasonal, atmospheric, or sensor differences.

## Slide 9
EXAMPLE ACCEPTANCE CRITERIA
Quality gate: comparability is measured
Geospatial Building Block | Sentinel-2 + DJI
9
PIXEL GRID
Exact equality
REGISTRATION RMSE
< 1 target pixel
COMMON OVERLAP
>= 10,000 pixels
HISTOGRAM DISTANCE
JS <= 0.10 / band
CLIPPING
<= 1%
CLOUD + SHADOW
<= 5%
Thresholds are deployment parameters, not universal accuracy claims.

## Slide 10
EVIDENCE ACCOMPANIES EVERY DERIVED IMAGE
What the execution produces
Geospatial Building Block | Sentinel-2 + DJI
10
RASTER
Cloud Optimized GeoTIFF Exact target grid + overviews
CATALOG
STAC Item Geometry + projection + asset checksum
QUALITY
Pixel overlap + RMSE JS distance + clipping + masks
PROVENANCE
Input/output SHA-256 Method + model identity + run ID
Fixture result
65,536
overlap pixels
0.138 -> 0.0043
worst-band JS distance
0%
clipping
PASS
all gates
A deliberately tightened JS threshold returns exit code 2 and a machine-readable failed report.

## Slide 11
CWL LOCALLY; REANA PACKAGING SUPPLIED
How it executes today
Geospatial Building Block | Sentinel-2 + DJI
11
1. RUN SENTINEL-2
Produces target_grid.json and reference_histogram.json
2. TRANSFER CONTRACTS
Checksum and upload to the second REANA run
3. RUN DJI
Produces matched COG and QC evidence
LOCAL
• cwltool executes now
• run_demo.py chains both runs
• CWL stages scripts explicitly
• Failure gates return nonzero
REANA
• Two descriptors supplied
• Reference assets transfer between runs
• Worker image must include dependencies
• Runtime logs augment provenance
API FACADE
• Kernel metadata is registered
• Existing facade proves job pattern
• Harmonization endpoints remain next
• Bindings are target capabilities
Current API boundary: direct CWL execution works; dedicated harmonization facade endpoints are not yet implemented.

## Slide 12
WHAT EXISTS AND WHAT REMAINS
Executable package and production boundary
Geospatial Building Block | Sentinel-2 + DJI
12
RUN NOW
• workflows/imagery_harmonization/run_demo.py
• sentinel2-workflow.cwl + dji-workflow.cwl
• Rasterio COG/grid/histogram processing
• TorchScript interface and model provenance
• Positive and failure acceptance behavior
PRODUCTION INTEGRATION
• Validated Sentinel-2 model + completed model card
• ODM/WebODM orthomosaic and checkpoint report
• Tiled model inference for large scenes
• Published REANA worker image
• Facade process endpoints and field calibration
python3 workflows/imagery_harmonization/run_demo.py